## Slide 1: 網管會議
2015/04/10

## Slide 2: 校園網路常見問題
校內交換器階層數過多或規劃不良
網路線過長未使用光纖
網路線材使用100M
佈線未編號及線路來源目標不清楚
教室預留資訊座過少
交換器與節點設備直接連接，未使用跳線面板
網路線未使用適當管路包覆
網段未適當切割，同一網段節點數過多
使用IP分享器切割校內網段
無線網路設定與規劃不良

## Slide 3: 網路速度測試
關閉防毒軟體
測速網站
http://spt.ntct.edu.tw
http://ftp.ntct.edu.tw
http://speedtest.net

## Slide 4: 資訊安全
防火牆規則
管理者密碼、規則
Windows XP
免費軟體的問題
伺服器服務漏洞
DNS黑名單
入侵偵測系統
黑名單IP阻擋

## Slide 5: 縣網服務
PROXY
http://proxy.ntct.edu.tw/proxy.pac
Windows Update
開始>gpedit.msc>電腦設定>系統管理範本 Windows元件>Windows Update>指定內部近端網路更新服務
或使用Windows更新登錄檔

## Slide 6: 無線網路
縣網無線網路控制器
start rolling upgrade
AP越多越好？
TANetRoaming（Web認證）、Eduroam（802.1x認證）
防火牆內對外需開放連接163.22.168.174 tcp 8080、tcp 8443、udp 3478

## Slide 7: 防火牆
提供校園主機安全性
pfSense 效能與穩定性
設定檔匯入
Botnet、Malware、Phishing IP黑名單、DNS 黑名單
URL 過濾
OpenVPN
網路分流
暑期研習

## Slide 8: 工業型機架主機

## Slide 9: 中大型學校
1U Rackmount 4 LAN Ports Network Appliance
Onboard Intel® Atom™ C2558/C2758 Quad-Core/ Octo-Core 2.4GHz SoC Processor
240-Pin Single Channel DDR3L 1600MHz DIMM x 4, Up to 64 GB
Gigabit Ethernet x 4
Optional Up to 2 Pairs LAN Bypass Function
3.5” SATA HDD x 1 or 2.5” SATA HDD x 2 and CF Socket x 1
RJ-45 Console x 1, USB2.0 x 2
Optional NIM Slot x 1
Optional PCI-E ﹝x4﹞ x 1
ATX PSU 100W
Mini-PCIe Slot x 1

## Slide 10: 小型學校
Onboard Intel Atom C2358 Dual Core 1.7 GHz SoC Processor
240-pin ECC DDR3 DIMM or non-ECC SDRAM, Up to 16GB
Built-in Gigabit Ethernet x 6
Supports QuickAssist Crypto Acceleration
Built-in Intel® i211AT LAN Controller and Marvell PHY 88E1543
System Cooling Fan x 1
Supports 2 Pairs with LAN Bypass Function
Compact Desktop Design

## Slide 11: 網路模組